1	gesis® IP+ - Circular connector system IP66/68 - 3-pole - RST25i3	2

1.1	Connector	2

1.1.1	Cable diameter 10-14 mm	2

1.1.1.1	Female with screw connection	2

1.1.1.2	Male with screw connection	3

1.1.2	Cable diameter 13-18 mm	4

1.1.2.1	Female with screw connection	4

1.1.2.2	Male with screw connection	5

1.2	Device connector	6

1.2.1	M25	6

1.2.1.1	Female with screw connection	6

1.2.1.2	Male with screw connection	7

1.3	Distribution block	8

1.4	Cable assemblies	9

1.4.1	Cable assemblies, 4.0 mm², containing halogen	9

1.4.2	Cable assemblies, 4.0 mm², insulating rubber compound	11

2	gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST25i5	13

2.1	Connector	13

2.1.1	Cable diameter 10-14 mm	13

2.1.1.1	Female with screw connection	13

2.1.1.2	Male with screw connection	14

2.1.2	Cable diameter 13-18 mm	15

2.1.2.1	Female with screw connection	15

2.1.2.2	Male with screw connection	16

2.2	Device connector	17

2.2.1	M25	17

2.2.1.1	Female with screw connection	17

2.2.1.2	Male with screw connection	18

2.3	Distribution block	19

2.4	Cable assemblies	20

2.4.1	Cable assemblies, 4.0 mm², containing halogen	20

2.4.2	Cable assemblies, 4.0 mm², insulating rubber compound	22

# gesis® IP+ - Circular connector system IP66/68 - 3-pole - RST25i3

## Connector

## Cable diameter 10-14 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S B1 ZR2SV GR03

Part No.: 96.031.4154.3

### Male with screw connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S S1 ZR2 V BG03

Part No.: 96.032.4154.3

## Cable diameter 13-18 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S B1 ZR3SV GR03

Part No.: 96.031.4554.3

### Male with screw connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S S1 ZR3SV BG03

Part No.: 96.032.4554.3

## Device connector

### M25

### Female with screw connection

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 6.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S B1 M01V GR03

Part No.: 96.031.5054.3

### Male with screw connection

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 25 A, 32 A with 6 mm²

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A, 32 A with 6 mm²

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 6.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I3S S1 M01V GR03

Part No.: 96.032.5054.3

## Distribution block

gesis® Distribution block, IP66/68, RST-Distribution box - RST RAN Solar

System gesis® IP+ - Distribution unit RST RAN Solar, coding concrete gray.

Rated voltage: 250 V

Rated current: 25 A

Inputs: 6 (RST25i3, concrete gray)

Cable glands: 1x M40, 2x M20

Connection clamps: 5x 35 mm²

Circuit breakers: 6x B25A

Dimension: 350x300x100 mm

Sheet metal: powder-coated, RAL7032

Brand: Wieland Electric GmbH

Type: RST25I3 X6B25A

Part No.: 99.512.0000.7

gesis® Distribution block, IP66/68, Distribution box RST Solar

System gesis® IP+ - Distribution unit RST RAN Solar.

Rated voltage: 250 V

Rated current: 25 A

Inputs: 3 (RST25i3, concrete gray)

Cable glands: 1x M32, 2x M20

Connection clamps: 5x 10 mm²

Dimension: 180x180x90 mm

Plastic

Brand: Wieland Electric GmbH

Type: RST25I3 1xE3xA

Part No.: 99.502.0000.7

## Cable assemblies

### Cable assemblies, 4.0 mm², containing halogen

gesis® extension cable IP66/68, female, male, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 3-pole, 4.0 mm², with locking, male RST25i3, female RST25i3, according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KSBS 40P xxBG03

Part No.: 96.834.xx00.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, female, free end, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 4.0 mm², female RST25i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KSB- 40P xxBG03

Part No.: 96.834.xx03.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, male, free end, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 4.0 mm², with locking, male RST25i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KS-S 40P xxBG03

Part No.: 96.834.xx04.3 (xx corresponds to length in dm, 0.5 m steps)

### Cable assemblies, 4.0 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 3-pole, 4.0 mm², with locking, male RST25i3, female RST25i3, according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KSBS 40 xxBG03

Part No.: 96.834.xx30.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, female, free end, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 4.0 mm², female RST25i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KSB- 40 xxBG03

Part No.: 96.834.xx33.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, male, free end, 3x 4.0 mm², 250 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 4.0 mm², with locking, male RST25i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I3KS-S 40 xxBG03

Part No.: 96.834.xx34.3 (xx corresponds to length in dm, 0.5 m steps)

# gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST25i5

## Connector

## Cable diameter 10-14 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 4.0 mm² (without ferrules)

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S B1 ZR2S BG03

Part No.: 96.051.4154.3

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 4.0 mm² (without ferrules)

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S S1 ZR2SV BG03

Part No.: 96.052.4154.3

## Cable diameter 13-18 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 4.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S B1 ZR3S BG03

Part No.: 96.051.4554.3

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S6B1 ZR3SV GR03

Part No.: 99.575.0000.7

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 4.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S S1 ZR3SV BG03

Part No.: 96.052.4554.3

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: up to 6.0 mm² (without ferrules)

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S6S1 ZR3SV GR03

Part No.: 99.576.0000.7

## Device connector

### M25

### Female with screw connection

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 4.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S B1 M01V GR03

Part No.: 96.051.5054.3

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 6.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25i5S6B1 M01V GR03

Part No.: 99.577.0000.7

### Male with screw connection

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 4.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25I5S S1 M01V BG03

Part No.: 96.052.5054.3

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 25 A

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: up to 6.0 mm² (without ferrules)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE, 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST25i5S6S1 M01V GR03

Part No.: 99.578.0000.7

## Distribution block

gesis® Distribution block, IP66/68, RST-Distribution box - RST RAN Solar

System gesis® IP+ - Distribution unit RST RAN Solar, coding concrete gray.

Rated voltage: 250/400 V

Rated current: 25 A

Inputs: 6 (RST25i5, concrete gray)

Cable glands: 1x M40, 2x M20

Connection clamps: 5x 35 mm²

Circuit breakers: 6x B25A

Dimension: 500x300x120 mm

Sheet metal: powder-coated, RAL7032

Brand: Wieland Electric GmbH

Type: RST25I5 X6B25A

Part No.: 99.527.0000.7

gesis® Distribution block, IP66/68, Distribution box RST Solar

System gesis® IP+ - Distribution unit RST RAN Solar.

Rated voltage: 250/400 V

Rated current: 25 A

Inputs: 3 (RST25i5, concrete gray)

Cable glands: 1x M32, 2x M20

Connection clamps: 5x 10 mm²

Dimension: 180x180x90 mm

Plastic

Brand: Wieland Electric GmbH

Type: RST25I5 1xE3xA

Part No.: 99.528.0000.7

## Cable assemblies

### Cable assemblies, 4.0 mm², containing halogen

gesis® extension cable IP66/68, female, male, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST25i5, female RST25i5, according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KSBS 40P xxBG03

Part No.: 96.854.xx00.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, female, free end, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST25i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KSB- 40P xxBG03

Part No.: 96.854.xx03.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, male, free end, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST25i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KS-S 40P xxBG03

Part No.: 96.854.xx04.3 (xx corresponds to length in dm, 0.5 m steps)

### Cable assemblies, 4.0 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST25i5, female RST25i5, according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KSBS 40 xxBG03

Part No.: 96.854.xx30.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, female, free end, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST25i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KSB- 40 xxBG03

Part No.: 96.854.xx33.3 (xx corresponds to length in dm, 0.5 m steps)

gesis® connection cable IP66/68, male, free end, 3x 4.0 mm², 250/400 V, 25 A, length: xx dm, concrete gray/black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST25i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding concrete gray/black.

Rated voltage: 250/400 V

Rated current: 25 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: xx dm

Brand: Wieland Electric GmbH

Type: RST25I5KS-S 40 xxBG03

Part No.: 96.854.xx34.3 (xx corresponds to length in dm, 0.5 m steps)

96.031.4154.3	2

96.031.4554.3	4

96.031.5054.3	6

96.032.4154.3	3

96.032.4554.3	5

96.032.5054.3	7

96.051.4154.3	13

96.051.4554.3	15

96.051.5054.3	17

96.052.4154.3	14

96.052.4554.3	16

96.052.5054.3	18

96.834.xx00.3	9

96.834.xx03.3	9

96.834.xx04.3	10

96.834.xx30.3	11

96.834.xx33.3	11

96.834.xx34.3	12

96.854.xx00.3	20

96.854.xx03.3	20

96.854.xx04.3	21

96.854.xx30.3	22

96.854.xx33.3	22

96.854.xx34.3	23

99.502.0000.7	8

99.512.0000.7	8

99.527.0000.7	19

99.528.0000.7	19

99.575.0000.7	15

99.576.0000.7	16

99.577.0000.7	17

99.578.0000.7	18