1	gesis® IP+ - Circular connector system IP66/68 - 4-pole - RST50i4	2

1.1	Connector	2

1.1.1	Cable diameter 15-25 mm	2

1.1.1.1	Female with screw connection	2

1.1.1.2	Female with crimp connection	3

1.1.1.3	Male with screw connection	4

1.1.1.4	Male with crimp connection,	5

1.1.2	Cable diameter 20-32 mm	6

1.1.2.1	Female with screw connection	6

1.1.2.2	Female with crimp connection	7

1.1.2.3	Male with screw connection	8

1.1.2.4	Male with crimp connection,	9

1.2	Device connector	10

1.2.1	M32	10

1.2.1.1	Female with screw connection	10

1.2.1.2	Female with crimp connection	11

1.2.1.3	Male with screw connection	12

1.2.1.4	Male with crimp connection,	13

1.3	Accessories	14

2	gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST50i5	16

2.1	Connector	16

2.1.1	Cable diameter 15-25 mm	16

2.1.1.1	Female with screw connection	16

2.1.1.2	Female with crimp connection	17

2.1.1.3	Male with screw connection	18

2.1.1.4	Male with crimp connection,	19

2.1.2	Cable diameter 20-32 mm	20

2.1.2.1	Female with screw connection	20

2.1.2.2	Female with crimp connection	21

2.1.2.3	Male with screw connection	22

2.1.2.4	Male with crimp connection,	23

2.2	Device connector	24

2.2.1	M32	24

2.2.1.1	Female with screw connection	24

2.2.1.2	Female with crimp connection	25

2.2.1.3	Male with screw connection	26

2.2.1.4	Male with crimp connection,	27

2.3	Accessories	28

# gesis® IP+ - Circular connector system IP66/68 - 4-pole - RST50i4

## Connector

## Cable diameter 15-25 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S B1 ZR5 S SW

Part No.: 97.041.4053.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C B1 ZR5 S SW

Part No.: 97.141.0053.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S S1 ZR5 S SW

Part No.: 97.042.4053.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C S1 ZR5 S SW

Part No.: 97.142.0053.1

## Cable diameter 20-32 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S B1 ZR6 S SW

Part No.: 97.041.4253.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C B1 ZR6 S SW

Part No.: 97.141.0253.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S S1 ZR6 S SW

Part No.: 97.042.4253.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C S1 ZR5 S SW

Part No.: 97.142.0253.1

## Device connector

## M32

### Female with screw connection

gesis® Device connector, IP66/68, female, 4-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S B1 ZM02V SW

Part No.: 97.041.5553.1

gesis® Device connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S B1 M02V SW

Part No.: 97.041.5053.1

### Female with crimp connection

gesis® Device connector, IP66/68, female, 4-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C B1 ZM02V SW

Part No.: 97.141.1553.1

gesis® Device connector, IP66/68, female, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C B1 M02V SW

Part No.: 97.041.1053.1

### Male with screw connection

gesis® Device connector, IP66/68, male, 4-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 4-pole, turned contacts with screw connection fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S S1 ZM02V SW

Part No.: 97.042.5553.1

gesis® Device connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4S S1 M02V SW

Part No.: 97.042.5053.1

### Male with crimp connection,

gesis® Device connector, IP66/68, male, 4-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 4-pole, turned contacts with crimp connection, fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C S1 ZM02V SW

Part No.: 97.142.1553.1

gesis® Device connector, IP66/68, male, 4-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I4C S1 M02V SW

Part No.: 97.042.1053.1

## Accessories

gesis® cover IP66/68 for female/male, 2-3-pole, black

System gesis® IP+ - Cover IP66/68 for female/male parts RST50i4 and RST50i5, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50 VS SW

Part No.: Z5.567.5653.0

gesis® crimp contact, female, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C B 40

Part No.: 02.126.0621.8

gesis® crimp contact, female, 6.0 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST50, with marking 1 (groove).

Terminal cross-section, fine-stranded: 6.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST50C B 60

Part No.: 02.126.0721.8

gesis® crimp contact, female, 10.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 10.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C B 00

Part No.: 02.126.0821.8

gesis® crimp contact, male, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C S 40

Part No.: 05.545.2821.8

gesis® crimp contact, male, 6.0 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST50, with marking 1 (groove).

Terminal cross-section, fine-stranded: 6.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST50C S 60

Part No.: 05.545.2921.8

gesis® crimp contact, male, 10.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 10.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C S 00

Part No.: 05.545.3021.8

gesis® adapter ring, 40 mm

System gesis® IP+ - Adapter ring for fixing the device connector inside 40 mm knock-outs, black.

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50

Part No.: 05.568.1853.0

Crimping tool - Crimping tool incl. system kit

Crimping tool - Crimping tool including system kit.

Brand: Wieland Electric GmbH

Part No.: 95.101.0800.0

Crimping tool - Crimping die D

Crimping tool - Crimping die D.

Brand: Wieland Electric GmbH

Part No.: 05.502.2300.0

# gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST50i5

## Connector

## Cable diameter 15-25 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S B1 ZR5 S SW

Part No.: 97.051.4053.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C B1 ZR5 S SW

Part No.: 97.151.0053.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S S1 ZR5 S SW

Part No.: 97.052.4053.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C S1 ZR5 S SW

Part No.: 97.152.0053.1

## Cable diameter 20-32 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S B1 ZR6 S SW

Part No.: 97.051.4253.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C B1 ZR6 S SW

Part No.: 97.151.0253.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (solid/stranded): 4.0 - 6.0 mm²

Terminal cross-section (flexible wires): 4.0 - 16.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S S1 ZR6 S SW

Part No.: 97.052.4253.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Circular connector with type of protection IP66/IP68, male, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 20 - 32 mm

Cable gland: M40

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C S1 ZR5 S SW

Part No.: 97.152.0253.1

## Device connector

## M32

### Female with screw connection

gesis® Device connector, IP66/68, female, 5-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S B1 ZM02V SW

Part No.: 97.051.5553.1

gesis® Device connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S B1 M02V SW

Part No.: 97.051.5053.1

### Female with crimp connection

gesis® Device connector, IP66/68, female, 5-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C B1 ZM02V SW

Part No.: 97.151.1553.1

gesis® Device connector, IP66/68, female, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C B1 M02V SW

Part No.: 97.051.1053.1

### Male with screw connection

gesis® Device connector, IP66/68, male, 5-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S S1 ZM02V SW

Part No.: 97.052.5553.1

gesis® Device connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding black.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5S S1 M02V SW

Part No.: 97.052.5053.1

### Male with crimp connection,

gesis® Device connector, IP66/68, male, 5-pole, 250/400 V, 50 A, fixed in position

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 5-pole, turned contacts with crimp connection, fixed in position, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section (flexible wires): 4.0 - 10.0 mm²

Cable diameter: 15 - 25 mm

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C S1 ZM02V SW

Part No.: 97.152.1553.1

gesis® Device connector, IP66/68, male, 5-pole, 250/400 V, 50 A

System gesis® IP+ - Device connector with type of protection IP66/IP68, male, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding black. Crimp contacts have to be ordered separately.

Rated voltage: 250/400 V

Rated current: 50 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 4.0 - 16.0 mm²

Cable gland: M32

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 1, 2, 3, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50I5C S1 M02V SW

Part No.: 97.052.1053.1

## Accessories

gesis® Cover IP66/68 for female/male, 2-3-pole, black

System gesis® IP+ - Cover IP66/68 for female/male parts RST50i4 and RST50i5, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50 VS SW

Part No.: Z5.567.5653.0

gesis® crimp contact, female, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C B 40

Part No.: 02.126.0621.8

gesis® crimp contact, female, 6.0 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST50, with marking 1 (groove).

Terminal cross-section, fine-stranded: 6.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST50C B 60

Part No.: 02.126.0721.8

gesis® crimp contact, female, 10.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 10.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C B 00

Part No.: 02.126.0821.8

gesis® crimp contact, male, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C S 40

Part No.: 05.545.2821.8

gesis® crimp contact, male, 6.0 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST50, with marking 1 (groove).

Terminal cross-section, fine-stranded: 6.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST50C S 60

Part No.: 05.545.2921.8

gesis® crimp contact, male, 10.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST50, without marking (groove).

Terminal cross-section, fine-stranded: 10.0 mm²

Brand: Wieland Electric GmbH

Type: RST50C S 00

Part No.: 05.545.3021.8

gesis® adapter ring, 40 mm

System gesis® IP+ - Adapter ring for fixing the device connector inside 40 mm knock-outs, black.

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST50

Part No.: 05.568.1853.0

Crimping tool - Crimping tool incl. system kit

Crimping tool - Crimping tool including system kit.

Brand: Wieland Electric GmbH

Part No.: 95.101.0800.0

Crimping tool - Crimping die D

Crimping tool - Crimping die D.

Brand: Wieland Electric GmbH

Part No.: 05.502.2300.0

Sample kit RST50i5

Sample kit RST50i5 - Complete kit including: connector, device connector, cover piece and knock-out (metal sheet)

Brand: Wieland Electric GmbH

Part No.: 99.628.0000.0

02.126.0621.8	14, 28

02.126.0721.8	14, 28

02.126.0821.8	14, 28

05.502.2300.0	15, 29

05.545.2821.8	14, 28

05.545.2921.8	15, 29

05.545.3021.8	15, 29

05.568.1853.0	15, 29

95.101.0800.0	15, 29

97.041.1053.1	11

97.041.4053.1	2

97.041.4253.1	6

97.041.5053.1	10

97.041.5553.1	10

97.042.1053.1	13

97.042.4053.1	4

97.042.4253.1	8

97.042.5053.1	12

97.042.5553.1	12

97.051.1053.1	25

97.051.4053.1	16

97.051.4253.1	20

97.051.5053.1	24

97.051.5553.1	24

97.052.1053.1	27

97.052.4053.1	18

97.052.4253.1	22

97.052.5053.1	26

97.052.5553.1	26

97.141.0053.1	3

97.141.0253.1	7

97.141.1553.1	11

97.142.0053.1	5

97.142.0253.1	9

97.142.1553.1	13

97.151.0053.1	17

97.151.0253.1	21

97.151.1553.1	25

97.152.0053.1	19

97.152.0253.1	23

97.152.1553.1	27

99.628.0000.0	29

Z5.567.5653.0	14, 28